## Slide 1: GPC_4T General Purpose Compute Unit with 4 Hardware Threads
Adi Levy
Saar Kadosh
Adviser: Amichai Ben-David (Intel)

## Slide 2: Project Introduction

## Slide 3: Introduction
Main Idea
General Purpose Compute Unit
RISC-V 32i Core with 4 hardware threads
Data & Instruction Memories
Integration Ability to RC – Ring Controller
With RC integration – a LOTR Tile – piece of the LOTR Project

## Slide 4: Introduction
LOTR Project
FABRIC
Ring Architecture

## Slide 5: Introduction
Project’s Structure
HIGH-LEVEL-SPECIFICATIONS (HAS)
MICRO-ARCHITECTURE-SPECIFICATIONS (MAS)
VALIDATION PLAN
DEVELOPMENT ENVIRONMENT & METHODOLOGIES

## Slide 6: HAS

## Slide 7: HIGH-LEVEL-SPECIFICATIONS
3 Main building block
Core
D MEM WRAP
I MEM WRAP

## Slide 8: HIGH-LEVEL-SPECIFICATIONS
2 Standard interfaces from RC
Core
D MEM WRAP
I MEM WRAP
Ring

## Slide 9: RISC – V 32i
Compatible with the RISCV ISA - RV32I

## Slide 10: RISC – V 32i
an open-source base-integer instruction set architecture (ISA)
RISC V assembly commands encoded to 32-bit
5 types of 32 bits encoded commands
RISC V32i commands can be found here
RV32I support only integer based. Gpc_4T does not support RISC-V 32M which support multiplication command or RISC V-32F

## Slide 11: Multithreading
Multithreading – Fine Grain Multithreading
Cyclic order. 1 thread per cycle – single scalar
©Image from Prof. Freddy Gabbay’s lectures on computer architectures

## Slide 12: Multithreading
No Data hazards
Each thread has is own PC and registers
Each thread has its own stack base address in data memory
All threads share resources
©Image from Prof. Freddy Gabbay’s lectures on computer architectures

## Slide 13: Pipeline
In – Order Pipeline with 5 stages:
Fetch
Decode
Execute
Memory
Write-Back
IPC = 1 IPC/Thread = 1/4
F
D
E
M
WB

## Slide 14: Building Blocks
Core
5 Pipe stages – Q100H, Q101H, Q102H, Q103H, Q104H,
Memory modules integrated

## Slide 15: Memory Modules
Address space:
32 bits addressing
Offset – 12 bits – for data and instruction memory (4KB)
Region – 2 bits – request destination:
  00 – I Mem
  01 – D Mem
  11 – CR Mem
Core Id – 8 bits – unique core id for each core in the LOTR fabric
Reserved – for future possible additions
Memory Offset | reserved | Region | Core ID
Address[11:0] | Address[21:12] | Address[23:22] | Address[31:24]

## Slide 16: Memory Modules
Instruction Memory (I MEM) & Data Memory (DMEM)
4KB Sized Memory
S-RAM based
Dual port – input and output (core and RC)
S-RAM Instruction Memory
Offset : 0x0000_0000
Encoded Region : 00
Offset : 0x0040_0000
Encoded Region : 01
S-RAM Data Memory

## Slide 17: Memory Modules
I MEM Wrap
Encapsulate the I MEM module
Has interface with the core and with the Ring controller
I mem
Core
Ring
W
R

## Slide 18: Memory
Control registers Memory (CR MEM)
Unique memory region for special requests
Flip Flop based memory – all data saved in flops
Holds control read only data such as current running thread and core, each thread’s PC, etc.
Control writable flops with abilities such freeze and reset PC for each thread.
Core and Ring access

## Slide 19: Memory Modules
D MEM Wrap
Encapsulate the D MEM and the CR MEM modules
Has interface with the core and with the Ring controller
Take care of Non-local memory transactions.
D mem
Cr
Comb. Logic
Core
Ring
R/W
R/W

## Slide 20: Supported features
CR table & functionality
Offset | Name | Type | Structure
0 | WHO_AM_I | RO | [15:0]
4 | CR_THREAD_ID | RO | [1:0]
8 | CR_CORE_ID | RO | [7:0]
C | CR_STACK_BASE_OFFSET | RO | [15:0]
10 | CR_TLS_BASE_OFFSET | RO | 
14 | CR_SHARED_BASE_OFFSET | RO | [15:0]
18 | CR_I_MEM_MSB | RO | [7:0]
20 | CR_D_MEM_MSB | RO | [7:0]
24 | CR_THREAD<id>_STATUS | RO | [7:0]
110 114 118 11c | CR_THREAD<id>_EXCEPTION_CODE | RO | [31:0]
120 124 128 12c | CR_THREAD<id>_PC_RST | RW | [0]
130 134 138 13c | CR_THREAD<id>_PC_EN | RW | [0]
140 144 148 14c | CR_THREAD<id>_DFD_REG_ID | RW | [4:0]
150 154 158 15c | CR_THREAD<id>_PC | RO | [31:0]

## Slide 21: Other Features
  Non-local memory access via Ring Controller
  Freeze/reset PC of a thread from software (thru CR mem)
  Freeze/reset PC of a thread from hardware

## Slide 22: MAS

## Slide 23: Micro-Level Architecture

## Slide 24: Micro-Level Architecture
Logic Design implementation of GPC_4T Architectonic demands
HAS
MAS
I need 4 separate PCs

## Slide 25: Design Building Blocks
Main blocks:
Core_4t – RISC V Core
D_Mem – data memory
CR_Mem – control registers memory
D_MEM_WRAP – wrapper for d_mem + cr_mem
I_Mem – Instruction memory
I_Mem_Wrap – wrapper for i_mem
GPC_4T – integration for core+wrappers

## Slide 26: Core block diagram

## Slide 27: Core block diagram
ADD x1 x2 x1

## Slide 28: Core Design
Thread switch - Scheduler:
Cycle 0 :
ThreadQ100H = 0001
NextThreadQ100H = 0010
Cycle 1 :
ThreadQ100H = 0010
NextThreadQ100H = 0100
Cycle N :
ThreadQ100H = 1000
NextThreadQ100H = 0001
ThreadQ101H = 0100
ThreadQ102H = 0010
ThreadQ103H = 0001
ThreadQ104H = 1000

## Slide 29: Core’s Pipe Stages
Fetch – Q100H
Maintain 4 Program counters
Next PC calculated on Q102H
Send PC to the I mem – request an instruction

## Slide 30: Pipe stages : Q100H
Next PC determine on Q102H

## Slide 31: Pipe stages : Q100H
PC’s Shalter:
Multithread – Pc enabled when thread’s turn
Freeze PC thru software from CR
Freeze PC from hardware – exmaple: reading from non-local core

## Slide 32: Pipe stages : Q100H
Nop is injected

## Slide 33: Pipe stages : Q100H
Insert Nop:
PC for thread 0 is disabled
Thread 0 is now at Q100H
Will bubble up the pipe until Q102H
insrtNopQ102H go to “En” PC0 flop

## Slide 34: Pipe stages : Q100H
Nop is injected

## Slide 35: Core’s Pipe Stages
Decode – Q101H
Receive 32-bit encoded instruction from i mem
Decode and extract relevant data from the instruction
Read relevant registers
Toggle the control signals

## Slide 36: Pipe stages : Q101H
I Mem
Instruction from I MEM
Decode data from I

## Slide 37: Pipe stages : Q101H
Registers numbers from decoded instruction

## Slide 38: Pipe stages : Q101H
Registers numbers from decoded instruction

## Slide 39: Pipe stages : Q101H

## Slide 40: Core’s Pipe Stages
Execute – Q102H
Arithmetic calculations with ALU
Next PC determination
Brach comparator

## Slide 41: Pipe stages : Q102H

## Slide 42: Core’s Pipe Stages
Memory – Q103H
Data memory (D mem) transaction
Data is read or written to the d mem

## Slide 43: Pipe stages : Q103H
Data Memory
MemRdDataQ103
Not much happened on the core

## Slide 44: Core’s Pipe Stages
Write Back – Q104H
Determine written data source – ALU, Memory, PC
Writes data in the registers

## Slide 45: Pipe stages : Q104H

## Slide 46: I Mem Design
Dual Port
2 Output flops
PC
ReadEN
Instruction Fetch
F2C address
WriteEn
F2C data
Write Data
Core
RC
Behavioral Memory - mem[SIZE_I_MEM-1:0];

## Slide 47: I Mem Design

## Slide 48: I Mem Wrap Design
I MEM instance
Core interface
Ring interface

## Slide 49: D Mem Design
Dual Port
Address
ReadEN
Read Data
Core
WriteEN
Write Data
ByteEN
RC
F2C Address
ReadEN
F2C Read Data
WriteEN
Write Data
ByteEN
Behavioral Memory - mem[SIZE_D_MEM-1:0];

## Slide 50: CR Mem Design
Big number of flops
Get data from hardware

## Slide 51: D Mem Wrap Design

## Slide 52: D Mem Wrap Design

## Slide 53: Supported features
Non-local memory access:
Read:
  Read request with core ID(bits 31:24) local core, will be directed by the D mem wrap to Ring Controller
  Requested thread’s PC will be frozen (“Nop injection”) until response arrives from RC
  Date read will written to registers in the Q104H stage
Write:
  write request with core ID(bits 31:24) local core, will be directed to Ring Controller
  No waiting for response – shoot and forget
  RC will pass the request to designated core’s memory

## Slide 54: Design Flows
Thread Freeze using CRs:
Thread can freeze other thread’s PC
Write `0 to CR space with offset:
Each PC flop Enable is fed from CR data
Offset | Name | Type | Structure
150 | THREAD<i>_PC_EN | RW | [0]
154 |  |  | 
158 |  |  | 
15c |  |  | 

## Slide 55: Thread Freeze using CRs:
Thread0 freeze Thread2 PC:
Write `0 to (0x00C00158).
MatchCrRegion signal invoked
On CR_MEM decode and write:
Offset | Name | Type | Structure
150 | THREAD<i>_PC_EN | RW | [0]
154 |  |  | 
158 |  |  | 
15c |  |  | 

## Slide 56: Thread Freeze using CRs:
Thread0 freeze Thread2 PC:
The `1 written is the enable bit for the En_PC2 flop
Thread0 written `0 will sampled by this flop
`0 will go to Core and disable the PC for thread 2

## Slide 57: Validation Plan

## Slide 58: Intro
How can we make sure are design will work as expected ?

## Slide 59: Intro
Validation !
Test bench to simulate GPC_4T
RISC V GCC to compile test C programs
Backdoor load file to the I mem (and Heap Mem)
Logs to track and verify behavior
Automation to make life easy

## Slide 60: GCC RISCV Compiler
GCC to generate test flow
Write c program dedicate to test a certain aspect in GPC_4T
Use RISC V WSL Toolchain to generate RISC V assembly file from C file
Use the Toolchain to generate 32 bits instruction sv file

## Slide 61: RISC V GNU Compiler Toolchain
Toolchain
Bundle of software tools cloned from "riscv-gnu-toolchain" Git repositories
Use GCC based compiler

## Slide 62: RISC V GNU Compiler Toolchain
Toolchain
C program
> RISC V assembly
> elf file
> binary sv file
Used by the Testbench as the instruction memory

## Slide 63: RISC V GNU Compiler Toolchain
WSL environment
Windows Subsystem Linux
We used Ubuntu
There are alternative – windows-based compilers

## Slide 64: RISC V GNU Compiler Toolchain
Compiling commands

## Slide 65: GCC RISCV Compiler

## Slide 66: GCC RISCV Compiler

## Slide 67: GCC RISCV Compiler

## Slide 68: GCC RISCV Compiler
Alive Test
Debug a program can be very complex
Alive Test is easy to debug
Simple RISC V commands
Runs and compare with expected results

## Slide 69: GCC RISCV Compiler
Alive Test
Simple commands
Easy expected results

## Slide 70: GCC RISCV Compiler
Multithread test – Matrix Multiplication
4x4 matrix multiply
Single thread code vs. parallel Multithread code
vs.

## Slide 71: GCC RISCV Compiler
Single thread

## Slide 72: GCC RISCV Compiler
Multithread:

## Slide 73: GCC RISCV Compiler
Winner:
Multithread

## Slide 74: System Verilog Test Bench
Gpc4t_tb.sv
Used for simulating the design (with ModelSim)
Instantiates the gpc_4t module
Generates clock and reset signals
Uses backdoor to inject instructions .sv file to i mem module
If necessary, use backdoor for heap data memory
Timeout for simulation defined there

## Slide 75: System Verilog Test Bench
Log generator
Initiate by the test bench
Sniff signals values and memory data from gpc_4t instantiated module using XMR
Use file system to create log files with the sampled data
Logs were our most important debug tool

## Slide 76: System Verilog Test Bench
Log examples:

## Slide 77: System Verilog Test Bench
End of Test Checker
At end of simulation, we compare generated memory snapshot to “golden memory snapshot”
“golden” is how we expect memory to be
If both are identical – test passed!
Else – time for debug….

## Slide 78: System Verilog Test Bench
Assertions
used to "catch" unwanted behavior and violations of the GPC_4T
implemented in the log generator
On some occasions – terminates the simulation

## Slide 79: System Verilog Test Bench
Assertions

## Slide 80: System Verilog Test Bench
RTL compilation
Prior to simulation, made by ModelSim
Compiles the test bench and all of the design Verilog files – Gpc_4t, Core, Memories, etc.
Can be performed with ModelSim GUI or with Windows PowerShell.

## Slide 81: System Verilog Test Bench
List.f

## Slide 82: System Verilog Test Bench
Simulation

## Slide 83: System Verilog Test Bench
Performed by ModelSim
GUI waveform, Log files
ADD x1(=4) x2(=5)

## Slide 84: Development & Methodologies

## Slide 85: Git & GitHub
Git
Software to track changes on shared files
GitHub
Internet hosting service provide git support
Maintain LOTR repository

## Slide 86: Git & GitHub
LOTR Repository

## Slide 87: Git & GitHub
Task Management

## Slide 88: Git & GitHub
Discussions

## Slide 89: Git & GitHub
Wikia

## Slide 90: RISC V GNU Compiler Toolchain
Toolchain
Discussed before

## Slide 91: System Verilog
Hardware Description Language
GPC_4T RTL (GPC_4T, Core, Memories)
GPC_4T test bench
GPC_4T defines and MACROs
FPGA synthesizable

## Slide 92: System Verilog
Coding Style
MACROs for flip-flops

## Slide 93: ModelSim
Environment for simulation HDL
elaboration, compilation, simulation
GUI, Waveform debug
PowerShell

## Slide 94: PowerShell & Bash
Automation scripts
Bash for scripting with Toolchain commands
PowerShell for scripting ModelSim commands
Enhance workflow

## Slide 95: PowerShell & Bash
Gpc_compile_link.sh
BASH language script
Initiate all Toolchain commands on C program
Creates folder for all test files(C, asm, sv, elf, etc)
Creates heap memory file if necessary by the program

## Slide 96: Future Plans
Project B - Implementation of an LOTR RISC-V Based System on Chip (SOC) on an FPGA
Architecture Optimize
New development environments (Windows)
RISC-V official
FPGA
More tests
More features

## Slide 97: Future Plans
LOTR Project
HW integration
Design and test on front door access
Enable non local memory access
Debug and clean SoC model from all core and RC bugs
Add new trackers on RC IO
Design IO tile and integrate into standard quartus IO interface
Compile& synthesize design on quartus env
SW stack from host side (from PC host to FPGA)

## Slide 98: Future Plans
Project B - Implementation of an LOTR RISC-V Based System on Chip (SOC) on an FPGA
Optimize arch of pipe
Support prevlidged CSR RISC V exten’ to allow OS
Use windows based Toolchain GCC (not WSL)
Move all WSL\PS scripts to simple bash script
Enable official riscv “competabillity test”
Test the design on FPGA:
  Syntisizable and timing convertion
Enable more complex mt tests
Support exception and error detections and inrretupts

## Slide 99: The End

## Slide 100: Question?